## Slide 1
BECE309L | AI & ML Course Project | VIT University
Hybrid Edge-AI Motor
Fault Detection &
Self-Healing System
Patent-Ready Implementation on ESP32
OneClassSVM · Mahalanobis · Physics Validation
4 Sensors · 7 Fault Types · 10 Patent Claims
98%
Classification
Accuracy
100%
Fault Recall
All 7 Types
4
Sensors
Integrated
10
Patent Claims
Implemented
₹2K
Total BOM
Cost
April 2026

## Slide 2
Presentation Outline
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
2 / 17
01
Problem Statement & Motivation
02
System Architecture & Block Diagram
03
Sensor Hardware & Acquisition
04
Edge-AI Inference Pipeline
05
ML Training — Google Colab
06
Performance Results
07
Patent Claims
08
Applications & SDG Mapping
09
Conclusion & Future Work

## Slide 3
Problem Statement & Motivation
Why do we need a better motor protection system?
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
3 / 17
THE PROBLEM
✕
Motors consume 40-50% of all global electricity
✕
Single motor trip can cost ₹5L–₹5Cr per hour
✕
Conventional relays detect only overcurrent / overtemp
✕
Cloud-based ML adds 50-500ms latency + privacy risk
✕
Commercial IEDs cost ₹30,000–₹5,00,000 per unit
OUR SOLUTION
✓
4-sensor multi-modal fault detection
✓
Edge-AI: 0ms cloud latency, full privacy
✓
7 fault types detected at 100% recall
✓
Self-healing: auto-restart, speed reduction
✓
Total BOM cost: under ₹2,000

## Slide 4
System Architecture — 5-Layer Design
Complete signal flow from physical plant to actuation
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
4 / 17
LAYER 0 — PHYSICAL PLANT
DC/BLDC Motor
Rotating Shaft
Drive Electronics
Mechanical Load
LAYER 1 — MULTI-SENSOR ACQUISITION (Claim 1)
IR Speed Sensor
GPIO 34
ACS712 Current
GPIO 35
MPU6050 Vibration
I2C 21/22
DS18B20 Temp
GPIO 4 OneWire
LAYER 2 — EDGE-AI INFERENCE (Claims 2, 3, 8)
OneClassSVM
micromlgen C model
Mahalanobis
Distance
Physics
Validation
Weighted
Fusion Score
LAYER 3 — FAULT CLASSIFICATION & ACTUATION (Claims 4, 5, 9)
Sev 0: Full Speed
Sev 1: Log+Alert
Sev 2: 50% Speed
Sev 3: Emergency Stop
LAYER 4 — PERSISTENCE & ADAPTATION (Claims 6, 7)
EEPROM Fault Log
20 records ring buffer
EMA Adaptive Baseline
α=0.05, N=100 cycles

## Slide 5
Hardware Platform — 4-Sensor ESP32 System
Claim 1: Multi-modal physical sensor acquisition
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
5 / 17
IR Speed Sensor
Pin: GPIO 34 Measures: RPM Formula: RPM = Pulses × 60000/Δt Detects: Stall, Overspeed
ACS712-30A
Pin: GPIO 35 (ADC1) Measures: Current (A) Formula: I = |Vadc−1.65| / 0.066 Detects: Overcurrent, Phase Loss
MPU6050 IMU
Pin: I2C SDA=21 SCL=22 Measures: Vibration (g RMS) Formula: Vib = √(Σ(|a|−1)²/N) Detects: Bearing Wear, Imbalance
DS18B20
Pin: GPIO 4 (OneWire) Measures: Temperature (°C) Formula: 12-bit, 0.0625°C res. Detects: Thermal Overload

## Slide 6
Edge-AI Inference Pipeline
Claims 2, 3, 8: Three-layer anomaly detection — entirely on ESP32
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
6 / 17
STEP 1
Normalize Input
z = (x−μ)/σ
StandardScaler constants
from Colab training
→
STEP 2
OneClassSVM
RBF kernel model
micromlgen C header
~0.8ms inference
→
STEP 3
Mahalanobis Dist.
χ²(0.995, df=4)
Threshold = 3.8549
Covariance envelope
→
STEP 4
Physics Validation
4 cross-sensor rules
Confidence 0.5–1.0×
Rejects sensor noise
→
STEP 5
Weighted Fusion
0.35·Vib + 0.30·Cur
+0.20·RPM+0.15·Temp
Score ∈ [0.0, 1.0]
SEVERITY THRESHOLDS
NOMINAL
Score: Score < 0.25
Full speed, update baseline
WARNING
Score: 0.25 – 0.50
Log event, blink LED
CRITICAL
Score: 0.50 – 0.75
Reduce speed to 50%
EMERGENCY
Score: > 0.75
Stop → cool-down → restart

## Slide 7
Fault Classification — Claim 4: Explainable Sensor-Rule Mapping
7 fault types, each traceable to a specific hardware sensor
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
7 / 17
Code
Fault Type
Trigger Sensor
Detection Rule
Severity
Action
0x01
Stall
IR Sensor
RPM < 50 while running
3 — Emergency
STOP → Restart
0x02
Overspeed
IR Sensor
RPM > 2400
2 — Critical
50% Speed
0x04
Overcurrent
ACS712
I > 12A
3 — Emergency
STOP → Restart
0x08
Phase Loss
ACS712
I < 0.4A when spinning
2 — Critical
50% Speed
0x10
Bearing Wear
MPU6050
Vibration RMS > 0.80g
2 — Critical
50% Speed
0x20
Thermal Overload
DS18B20
T > 65°C warn / 80°C stop
2-3
Reduce/STOP
0x40
ML Anomaly
All 4
OneClassSVM output = −1
1 — Warning
Log + Alert

## Slide 8
Adaptive Baseline + EEPROM Logging
Claims 6, 7: Self-calibration and persistent fault memory
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
8 / 17
CLAIM 7 — Adaptive EMA Baseline (α = 0.05)
Formula:
baseline_new = (1−α) × baseline_old + α × reading
updates every 100 normal cycles
α = 0.05 → slow, stable tracking
Compensates for motor aging, load drift,
bearing wear, temperature seasonal change
CLAIM 6 — EEPROM Persistent Fault Logging
timestamp_s
4 bytes
Uptime seconds
fault_code
1 byte
Bitmask of active faults
severity
1 byte
Level 0–3
score
4 bytes
Fusion score float
rpm_at_fault
4 bytes
RPM snapshot
action_taken
1 byte
0=none…3=restart
recovery_ok
1 byte
1=recovered, 0=manual
Ring buffer: 20 records max
Printed on every power-on boot

## Slide 9
ML Training — Google Colab Pipeline
4050-sample synthetic dataset → 3 trained models → C header files for ESP32
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
9 / 17
Cell 1
pip install libraries
Cell 3
Generate 4050-sample dataset
7 fault types × 150 samples + 3000 normal
Cell 5
StandardScaler → export #define constants
Cell 6
OneClassSVM → micromlgen → one_class_svm_model.h
Cell 7
Autoencoder 4→8→4→2→4→8→4 → TFLite INT8
Cell 8
Mahalanobis → chi-sq threshold 3.8549 → mahal_model.h
Cells 9-12
Ensemble fusion → ROC curves → weight sensitivity

## Slide 10
Performance Results
OneClassSVM achieves 98% accuracy with 100% recall on all fault types
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
10 / 17
98%
Overall Accuracy
100%
Fault Recall
97%
F1-Score
3%
False Positive Rate
OneClassSVM Classification Report (Colab Cell 6)
Mahalanobis Distance Report (Colab Cell 8)

## Slide 11
Per-Fault Detection — 100% Across All 7 Types
No missed fault — the core patent performance claim
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
11 / 17
Stall
100%
150 / 150 detected
Overspeed
100%
150 / 150 detected
Overcurrent
100%
150 / 150 detected
Phase Loss
100%
150 / 150 detected
Bearing Wear
100%
150 / 150 detected
Thermal
100%
150 / 150 detected
ML-Subtle
100%
150 / 150 detected
✓
Perfect
Detection
All 7 Types

## Slide 12
Patent Claims — All 10 Implemented
Each claim is traceable to a specific function in the ESP32 firmware
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
12 / 17
1
Multi-sensor acquisition
readRPM/Current/Vibration/Temperature()
2
Edge-only ML inference
one_class_svm_model.h in ESP32 flash
3
Weighted fusion score
W=0.35+0.30+0.20+0.15 → computeFusionScore()
4
Explainable fault classification
classifyFault() — 7 named sensor rules
5
Graduated corrective actuation
executeCorrectiveAction() sev 0/1/2/3
6
Persistent EEPROM logging
logFaultToEEPROM() FaultRecord ring buffer
7
Adaptive EMA baseline
updateAdaptiveBaseline() α=0.05 N=100
8
Physics cross-sensor validation
physicsValidationMultiplier() 4 rules
9
Dynamic thermal threshold
readTemperature() + thermal stop at 80°C
10
Autonomous recovery method
loop() — 8-step autonomous method

## Slide 13
ESP32 Runtime Performance & Cost Comparison
Validated hardware metrics vs. commercial alternatives
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
13 / 17
Sampling Rate
2 Hz (500ms)
ML Inference Time
~0.8 ms
EEPROM Write
~5 ms
Flash Usage
~380 KB
SRAM Used
~42 KB
Fault Log Capacity
20 records
Sampling Resolution
12-bit ADC
Cost Comparison vs. Commercial IEDs
Siemens SIMOCODE
₹3,00,000+
No Edge-AI, cloud needed
Schneider TeSys
₹1,50,000+
No adaptive baseline
ABB UMC100
₹80,000+
No self-healing logic
This System (ESP32)
< ₹2,000
ALL features, 100% edge
Cost saving: 98–99% vs. commercial alternatives

## Slide 14
Applications
Where this system creates real-world impact
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
14 / 17
Industrial
CNC Spindle Motors
Conveyor Drives
Compressors & Pumps
Cooling Tower Fans
Smart Buildings
HVAC Fan Coil Units
Elevator Drives
Water Pumping
Cold Storage Compressors
Agriculture
Irrigation Pump Motors
Grain Mill Drives
Crop Dryer Fans
Remote auto-restart
Research & EDU
AI/ML Lab Testbed
Motor Fault Research
Patent Prototype
IoT Teaching Kit
EV & Renewables
EV Traction Motors
Wind Turbine Bearings
Solar Tracker Drives
Battery Cooling Fans
Govt / Defense
Radar Motor Systems
Naval Pump Drives
Railway Traction
Smart Grid Motors

## Slide 15
SDG Mapping — Sustainable Development Goals
UN 2030 Agenda: 4 SDGs directly supported by this project
Hybrid Edge-AI Motor Fault Detection & Self-Healing System | BECE309L | VIT University
15 / 17
SDG
7
Affordable & Clean Energy
Motor efficiency + predictive maintenance reduces industrial electricity waste by 2-8% per unit
SDG
9
Industry, Innovation & Infrastructure
Edge-AI innovation, indigenous patent filing, reduces industry dependence on imported IEDs
SDG
11
Sustainable Cities & Communities
Smart city infrastructure protection: elevators, HVAC, water; digital maintenance records
SDG
12
Responsible Consumption
Extends motor lifespan, prevents premature e-waste, supports circular economy goals

## Slide 16
Conclusion
1
98% accuracy:
3-layer ensemble with 100% recall on all 7 fault types
2
10 patent claims:
Every claim implemented and verified in firmware
3
True edge-AI:
Zero cloud dependency — 0.8ms inference on ESP32
4
Self-healing:
Severity-graduated auto-restart with EEPROM forensic log
5
₹2,000 BOM:
1–2% of commercial IED cost — accessible to SMEs
Future Work: TFLite Autoencoder deployment · Wi-Fi telemetry · FFT vibration spectrum analysis

## Slide 17
Thank You
Questions & Discussion
Q: How does the system handle sensor failure?
A: Sensor validation checks reject out-of-range readings; each sensor's fault detection is independent.
Q: Can this be deployed on a real industrial motor?
A: Yes. Replace synthetic dataset with real motor data from the same GPIO pins; retrain in Colab and re-flash.
Q: What makes this patentable over prior art?
A: The specific combination of ESP32 + 4-sensor fusion + edge OneClassSVM + EMA adaptive baseline + EEPROM log + graduated self-healing is not described in prior art.
BECE309L — AI & ML Course Project | VIT University | April 2026